## Slide 1
Research objectives:
This research aims to enable indirect estimation of loads in complex mechanical systems, with a focus on bearings, using surface-mounted sensors and without modeling the rotating components. (The objective aims to bridge the gap caused by usage of expensive force cells to measure the applied loads to the system, as well as the experimental complexity associated with measurement of sensors placed in the harsh environment of rotating components (e.g. on the shaft inside gearboxes), and the numerical complexity of modeling these components.)
Research contribution:
We illustrate the influence and importance of a minimal reduction basis for load estimation, and introduce and analyze a novel reduction method for systems with periodic excitations.
We introduce a systematic framework for representative model building and updating, enabling identification of boundary conditions and guiding sensor placement with improved signal-to-noise ratio, improving the estimation performance from both modeling and measurement perspective.
We highlight the impact of sensors and their cables on the quality of acquired experimental data, particularly on damping parameters, and propose simple models to estimate or accurately account for this influence.
We apply the model generation framework and load estimation methodology to a setup with an industrial level of complexity and experimentally validate the bearing load estimation procedure.
Research approaches:
The observability of the reduced system based on the number of states is investigated. The reduction basis is concluded from basic equations on assumed loading conditions. In a numerical investigation, the performance of the novel reduction mode is investigated. The accuracy of the reduced mode is investigated depending on the accuracy of the detected frequency.
Starting from the discretized equations of motion, it is shown that the framework results in low uncertainty at each step. The boundary condition identification method is validated by a numerical example.
In an experimental investigation using laser doppler vibrometers, the influence of accelerometers and their cables are experimentally illustrated. A simple lumped parameter model for compensation is suggested, and the validity of the model is investigated.
By implementing the framework for model generation and updating as well as the boundary condition identification, sensor correlation on high SNR locations close to boundaries is permitted, and the lumped bearing load is estimated over a wide frequency range.
-

## Slide 2
Primary Objective:
  This research aims to enable the indirect estimation of loads in complex mechanical systems, with a specific focus on bearings. The methodology utilizes surface-mounted sensors to avoid the necessity of explicitly modeling rotating components.
Motivation:
The prohibitive cost of force cells for direct load measurement or, in some cases, infeasibility of it.
The experimental complexity of placing sensors in harsh environments (e.g., on shafts inside gearboxes).
The numerical cost and complexity associated with full-scale modeling of rotating components.
Research contributions and approaches:
Model reduction strategies: Contribution: We demonstrate the critical influence of a minimal reduction basis for load estimation and introduce a novel reduction method specifically designed for systems subject to periodic excitations. Approach: We investigate the observability of the reduced system as a function of the number of states. The reduction basis is analytically derived from fundamental equations based on assumed loading conditions. We then evaluate the performance of this novel reduction mode numerically, specifically quantifying the accuracy relative to the precision of the detected frequency.
Model updating and sensor placement: Contribution: We establish a systematic framework for representative model building and updating. This enables the precise identification of boundary conditions and guides sensor placement to maximize the Signal-to-Noise Ratio (SNR), thereby improving estimation performance from both modeling and measurement perspectives. Approach: Starting from discretized equations of motion, we demonstrate that this framework minimizes uncertainty at each stage. The validity of the boundary condition identification method is subsequently verified through numerical examples.
- Gemini’ed

## Slide 3
Experimental Fidelity (Cables & Damping): Contribution: We highlight the significant impact of sensors and their cabling on experimental data quality—particularly regarding damping parameters—and propose simplified models to accurately account for or compensate for these influences. Approach: Using Laser Doppler Vibrometers (LDV) for non-contact validation, we experimentally isolate the influence of accelerometers and their cables. We then propose and validate a simple lumped-parameter model to compensate for these mass and damping effects.
Industrial Validation: Contribution: We apply the model generation framework and load estimation methodology to a setup of industrial complexity, providing experimental validation for the bearing load estimation procedure. Approach: By implementing the full framework—including model updating and boundary condition identification—we enable sensor correlation at high-SNR locations near boundaries. This allows for the accurate estimation of the lumped bearing load over a wide frequency range.
- Gemini’ed

## Slide 4
On Objectives, Contributions and Approaches
Research objective(s):
The overarching aim or goal of this research is to […].
This goal can be supported by several specific objectives, typically grouped into focused research questions. These questions guide the inquiry and shape the structure of the dissertation, ensuring that each aspect of the research contributes meaningfully toward the overall aim.
Research contributions:
The contributions address the research objectives and provide novel understanding, methods, or tools relevant to the field. They present the learnings of the research.
Research approaches:
To validate the proposed contributions and support the research claims, a combination of approaches is employed. These approaches can be state-of-the-art.
Objective:
Which scientific gaps are addressed?
Contribution:
What claim is shown or debunked? What is illustrated? What are the key takeaways of the research?
Approach:
How is it validated or proven?
Approach:
Which SOTA methods have been applied?
Contribution:
Which learnings you had?
Approach:
How is the solution framework implemented?
Draft document: to be updated by LMSD

## Slide 5
On Objectives, Contributions and Approaches - Example
Research objectives:
This research aims to enable high-fidelity and bandwidth-aware estimation of states, inputs, and parameters in complex dynamical systems.
Research contribution:
We illustrate and exploit the interrelationship between the degree of observability of individual states, estimation performance and the impact on instrumentation.
Research approaches:
To achieve this, a novel Gramian-based observability metric is proposed for analyzing coupled vibroacoustic systems. This metric enables the identification of highly observable modes or states, particularly within specific frequency bands, enhancing estimation performance.
Experimental validation showns that the proposed criterion outperforms state-of-the-art observability metrics in sensor placement tasks, resulting in more accurate estimation of targeted states.
Draft document: to be updated by LMSD